## Slide 1: Component 3: Exercise Debrief
February 25, 2017

## Slide 2: Purpose of the SE ConOps Exercise
Introduce Systems Engineering
Perform ConOps Development Activities
Goal: Develop sections of a ConOps to describe the an ITS project for a major university trip generator – football game
Notes: Purpose of Slide: Review purpose of ConOps exercise.
Key Message: Review ConOps Exercise
Note to Instructor: The answers provided in this debrief and in the Instructor’s Version of the Exercise document represent just one possible solution set. There may be other answers that your students come up with. It is recommended that if a student’s answer is different than the one provided, it would be worth some time exploring the differences and why the student came to that solution which may be valid.
Time on Slide: 1 minutes
Suggested Comments: This case study introduces the Systems Engineering Process and explores the sections of a Concept of Operations.
This presentation will review each of the 4 tasks in the case study and provide an opportunity for students to ask questions and receive additional background on the various parts of the exercise. This debrief will help the students get the most out of the exercise.
It is important to stress to the class that this exercise is real-world and follows the Systems Engineering procedures that most transportation agencies or planning organizations would follow.
Transition:
Interactivity:
Additional Resources:

## Slide 3: Exercise Activities
  Task 1: Identify Stakeholders
    Determine who is involved
    Roles and Responsibilities
  Task 2: Current Situation
    Operations
    System Elements and Connections
  Task 3: Justification for Change
    User needs
    Description of Desired Changes
  Task 4: Concepts for Proposed System
    Policies and constraints impacting the system
    Description of the proposed system
Identify Stakeholders
Current Situation
Justification for Change
Concepts for Proposed System
Notes: Purpose of Slide: Describe the exercise tasks.
Key Message: The exercise consists of 4 Tasks.
Time on Chart: 1 minute
Suggested Comments: The exercise will consist of 4 tasks as listed on this slide. The objective is to define the concept of the project with added elements in each step.
Task 1 will identify the stakeholders.
Task 2 will explain the current situation.
Task 3 will produce a justification for changes.
Finally, Task 4 will develop supporting concepts for the proposed system.
Transition:
Interactivity:
Additional Resources:

## Slide 4: Task 1: Identify Stakeholders
The first step in developing a ConOps is identifying the stakeholders
This task requires you to read the project introduction and determine the possible stakeholders for the project
Identify Stakeholders
Current Situation
Justification for Change
Concepts for Proposed System
Notes: Purpose of Slide: Discuss Task 1 – Identify Stakeholders
Key Message: Identify Stakeholders
Time on Slide: 2 minutes
Suggested Comments: Understanding the stakeholders involved in the system operation is key to scoping the project and properly identifying user needs.
Transition:
Interactivity:
Additional Resources:

## Slide 5: Task 1: Identify Stakeholders
List of Stakeholders
City Department of Transportation/TMC Operators
City Police Department
State Department of Transportation
City Transit Department/Authority
City Parking Department/City Parking Operators
University Department of Transportation
University Parking Department
University Police Department
Travelers
Notes: Purpose of Slide: Identify Stakeholders
Key Message: Identify Stakeholders
Time on Slide: 2 minutes
Suggested Comments: The list of stakeholders can be derived or inferred from the project description.
Ask the class if anyone identified any other stakeholders…
Transition:
Interactivity:
Additional Resources:

## Slide 6: Task 1: Questions
Who is the stakeholder that is most central to the project?
Why could the State DOT be involved?
Is it a good idea to include transit stakeholders? Why or why not?
This may be obvious but it is important to identify the stakeholder that is central to the project, in this case the City DOT. Most successful projects have a champion stakeholder who has the overall responsibility for the project.
The State DOT usually is responsible for the freeways; since this project could impact the freeways and could provide additional field equipment in the vicinity of the freeway it is important to involve the State DOT.
Although it appears that this project is not primarily a transit project, the addition of field devices and an improved Traffic Management Center will benefit the City transit operations. Potentially sharing traffic conditions and camera images would enhance the overall traffic management around the stadium including transit.
Notes: Purpose of Slide: Review the Task 1 questions.
Key Message: Review the Task 1 questions.
Time on Slide: 4 minutes
Suggested Comments: Go over the questions and discuss the possible answers. Click to display potential answers.
Transition:
Interactivity: Ask class if they have any questions and encourage them to explain their answers.
Additional Resources:

## Slide 7: Task 2: Current Situation
The ConOps provides a common understanding of the environment that the project will be dealing with
The ConOps defines the scope of the project
Your task was to relate each stakeholder in Task 1 with their existing systems (center, traveler device, vehicle and/or a field device)
Identify Stakeholders
Current Situation
Justification for Change
Concepts for Proposed System
Notes: Purpose of Slide: Review Task 2: Determining the Current Situation
Key Message: For each stakeholder determined in the project, figure out their related systems.
Time on Slide: 1 minute
Suggested Comments: It is important to capture all the existing systems currently operated by the stakeholders that influence or are central to the project.
Transition:
Interactivity:
Additional Resources:

## Slide 8: Task 2: Current Situation
Stakeholder | Related ITS Systems
City Department of Transportation/TMC Operators | City Traffic Management Center City Cameras City Dynamic Message Signs City Vehicle Detectors
City Police Department | City 911 Call Center City Police Vehicles
State Department of Transportation | Freeway Traffic Management Center Freeway Cameras Freeway Dynamic Message Signs Freeway Vehicle Detectors
City Transit Department/Authority | City Transit Management Center City Transit Vehicles
City Parking Department/City Parking Operators | City Parking Occupancy Detectors
Notes: Purpose of Slide: Review Task 2: Current Situation.
Key Message: List of Related ITS Systems for each Stakeholder
Time on Slide: 1 minute
Suggested Comments: Here is the first page of the list of possible systems operated by each stakeholder (in no particular order).
Transition:
Interactivity:
Additional Resources:

## Slide 9: Task 2: Current Situation (cont.)
Stakeholder | Related ITS Systems
University Department of Transportation | University Traffic Management Center University Cameras University Dynamic Message Signs University Vehicle Detectors
University Parking Department | University Parking Occupancy Detectors
City Transit Department/Authority | City Transit Management Center City Transit Vehicles
University Police Department | University Police Vehicles
Travelers | Smart Phones/Devices
Notes: Purpose of Slide: Review Task 2: Current Situation.
Key Message: List of Related ITS Systems for each Stakeholder
Time on Slide: 1 minute
Suggested Comments: Here is the second page of the list of possible systems operated by each stakeholder (in no particular order).
Did anyone get anything different? If so, discuss as a class why or why not it may be appropriate.
Transition:
Interactivity:
Additional Resources:

## Slide 10: Task 3: Justification for Change
One of the most important parts of a ConOps is to capture the user (stakeholder) needs
User needs as well as the ConOps document must be written in the stakeholder’s language so it is easy for the users of the proposed system to understand
Remember to capture the User Needs, not the System Needs – System Requirements will be defined in the next systems Engineering step
Identify Stakeholders
Current Situation
Justification for Change
Concepts for Proposed System
Notes: Purpose of Slide: Discuss Task 3: Justification for Change
Key Message: It is important to justify any change to the current operations.
Time on Slide: 1 minutes
Suggested Comments: User needs are the key to ConOps development.
Transition:
Interactivity:
Additional Resources:

## Slide 11: Task 3: Justification for Change
Recall the Criteria for Writing a “Well-Written” User Need:
When documenting a user need, one must remember that it addresses an operational problem, and “describe” it using the following recommended criteria:
  Provide a structure by assigning a unique number and title to make it uniquely identifiable
  Identify a major desired capability (Including functions or features you desire from the device/system)
  Capture the rationale by stating why it is needed by the user
  Keep it solution-free: don’t get into how to meet it (design)
Notes: Purpose of Slide: Discuss Task 3: Justification for Change
Key Message: It is important to justify any change to the current operations.
Time on Slide: 1 minutes
Suggested Comments: User needs must be well-written and meet the recommended criteria:
Uniquely identifiable
Describe a major desired capability
Provide rationale
Solution-free
Transition:
Interactivity:
Additional Resources:

## Slide 12: Applying the Criteria: Transit AVL Example
in order for the transit vehicle to track its status against the route schedule and provide bus stop announcements.
UN 3.10 Configure Transit Vehicle Tracking System
Uniquely Identifiable
Major Desired Capability
Rationale
Solution-Free
Note that this user need does not specify how this will be accomplished,
it only specifies the user need.
The Transit Operator needs to enter the bus route information into the transit vehicle including the driver
12
Notes: Note that this slide reveals each line with a click of the mouse.
Suggested Comments: The Transit AVL example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: User Need (UN) 3.10 numbering and the title
  2. Major Desired Capability: The Transit Operator needs to enter the bus route information into the transit vehicle
  3. Capture Rationale: in order for the transit vehicle to track its status against its route schedule and provide bus stop announcements. The Rationale will help you develop the Validation cases for the user needs.
  4. Solution free, does not say how to accomplish the user need.

## Slide 13: Monitor Traffic Conditions Example
UN 3.4 Monitor Traffic Conditions
Uniquely Identifiable
The Traffic Management Center Operator needs to monitor and verify the traffic conditions around the stadium for both the freeway and arterial roadways
in order to better manage the traffic around the stadium.
Major Desired Capability
Rationale
Solution-Free
Note that this user need does not specify how this will be accomplished,
it only specifies the need.
13
Notes: Note that this slide reveals each line with a click of the mouse.
Key Message: This example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: UN 3.4 numbering and title
2. Major Desired Capability: The Traffic Management Center Operator needs to monitor and verify the traffic conditions around the stadium for both the freeway and arterial roadways
  3. Capture Rationale: in order to better manage the traffic around the stadium.
  4. Solution free, does not say how to accomplish the user need.

## Slide 14: Task 3: Your Turn
UN 3.7 Provide Traffic Condition Information to Travelers
Uniquely Identifiable
Travelers need traffic conditions in the vicinity of the stadium
in order to allow travelers to make informed decisions.
Major Desired Capability
Rationale
Solution-Free
Note that this user need does not specify how this will be accomplished,
it only specifies the need.
14
Notes: Note that this slide reveals each line with a click of the mouse.
Key Message: This example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: UN 3.7 numbering and title
2. Major Desired Capability: Travelers need traffic conditions in the vicinity of the stadium
  3. Capture Rationale: in order to allow travelers to make informed decisions.
  4. Solution free, does not say how to accomplish the user need.

## Slide 15: Task 3: Your Turn
UN 3.12 Monitor Transit Vehicles
Uniquely Identifiable
The Transit Management Center Operator needs to monitor its Transit Vehicles
in order to better manage the transit network and provide transit vehicle information to travelers.
.
Major Desired Capability
Rationale
Solution-Free
Note that this user need does not specify how this will be accomplished,
it only specifies the need.
15
Notes: Note that this slide reveals each line with a click of the mouse.
Key Message: This example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: UN 3.12 numbering and title
  2. Major Desired Capability: The Transit Management Center Operator needs to monitor its Transit Vehicles
  3. Capture Rationale: in order to better manage the transit network and provide transit vehicle information to travelers
  4. Solution free, does not say how to accomplish the user need.

## Slide 16: Task 3: Your Turn
UN 3.19 Exchange Traffic Condition Information between the Traffic Management and Transit Management Centers
Uniquely Identifiable
The Traffic Management Center Operator and Transit Management Center Operator need to share their traffic condition information with each other
in order to provide better traffic coordination around the stadium.
.
Major Desired Capability
Rationale
Solution-Free
Note that this user need does not specify how this will be accomplished,
it only specifies the need.
16
Notes: Note that this slide reveals each line with a click of the mouse.
Key Message: This example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: UN 3.19 numbering and title
  2. Major Desired Capability: The Traffic Management Center Operator and Transit Management Center Operator need to share their traffic condition information with each other
  3. Capture Rationale: in order to provide better traffic coordination around the stadium.
  4. Solution free, does not say how to accomplish the user need.

## Slide 17: Task 3: Your Turn
UN 3.4.1 Retrieve Remote Traffic Conditions using Cameras
Uniquely Identifiable
The City TMC Operator needs to remotely retrieve freeway and arterial roadway traffic conditions by controlling cameras
in order to obtain current roadway operational conditions.
.
Major Desired Capability
Rationale
Solution-Free???
Note that this user need does not specify how this will be accomplished,
it only specifies the need.
What is wrong with the following user need?
17
Notes: Note that this slide reveals each line with a click of the mouse.
Key Message: This example depicts a high level user need description and stresses all four elements of the criteria using animation
  1. Uniquely Identifiable: UN 3.4.1 numbering and title
  2. Major Desired Capability: The Transit Management Center Operator needs to monitor its Transit Vehicles
  3. Capture Rationale: in order to better manage the transit network and provide transit vehicle information to travelers
  4. Solution free???, does it say how to accomplish the user need? This user need assumes that cameras will be used to retrieve remote traffic conditions. Cameras may end up being used but the user need is to obtain remote traffic conditions, it may be better to use some sort of sensors or a combination of sensors and cameras…

## Slide 18: Task 4: Concepts for Proposed System
A high-level block diagram of the proposed system components helps to define the scope of the project.
Based on your understanding of the proposed project, sketch a rough block diagram of the major systems and the information they communicate with each other.
Make sure you label your system blocks as well as connecting the blocks where there is information communications between them.
Identify Stakeholders
Current Situation
Justification for Change
Concepts for Proposed System
Notes: Purpose of Slide: Introduce Task 4: Concepts for Proposed System
Key Message: Concepts for Proposed System
Time on Slide: 1 minutes
Suggested Comments: The concepts of the proposed system can be represented with high-level block diagrams illustrating the system involved and the connections between the systems to understand how they are related.
Transition:
Interactivity:
Additional Resources:

## Slide 19
City Traffic
Management Center
City Dynamic
Message Signs
City Vehicle
Detectors
City Parking
Occupancy
Detectors
City
Cameras
Freeway Traffic
Management Center
Freeway Dynamic
Message Signs
Freeway Vehicle
Detectors
Freeway
Cameras
Notes: The block diagrams on this page and the next 2 slides contain blocks for each ITS element or system. The blocks are connected together where information is exchanged. There are really two types of interfaces, center-to-field/vehicle and center-to-center. The center elements are colored green whereas the field devices and vehicles are colored blue. This slide contains the
City Traffic Management Center connected to
City Cameras
City Parking Occupancy Detectors
City Dynamic Message Signs
City Vehicle Detectors
Freeway Traffic Management Center connected to
Freeway Cameras
Freeway Dynamic Message Signs
Freeway Vehicle Detectors
Suggest class discussion on which elements currently exist and which elements are going to have new devices and connections.

## Slide 20
University Traffic
Management Center
University Dynamic
Message Signs
University Vehicle
Detectors
University Parking
Occupancy
Detectors
University
Cameras
City 9-1-1 Call Center
City Police Vehicles
University Police Vehicles
City Transit
Management Center
City Transit Vehicles
Notes: This slide contains the
University Traffic Management Center connected to
University Cameras
University Parking Occupancy Detectors
University Dynamic Message Signs
University Vehicle Detectors
City 911 Call Center connected to
City Police Vehicles
University Police Vehicles
City Transit Management Center connected to
City Transit Vehicles
Suggest class discussion on which elements currently exist and which elements are going to have new devices and connections.

## Slide 21
University Traffic
Management Center
City 9-1-1 Call Center
City Transit
Management Center
City Traffic
Management Center
Freeway Traffic
Management Center
Notes: This slide contains the center-to-center interfaces for the five centers:
City Traffic Management Center
City Transit Management Center
City 911 Call Center
University Traffic Management Center
Freeway Traffic Management Center
The center-to-center interfaces are important since they represent sharing of data and control between centers and agencies.
Suggest class discussion on which elements currently exist and which elements are going to have new devices and connections.

## Slide 22: Case Study Purpose
Provide understanding of systems engineering
Gain experience in beginning development of a systems project with a Concept of Operations
Explore balancing priorities in establishing project scope
Notes: Purpose of Slide: Conduct a review to ensure students got the purpose of the case study.
Key Message: Confirm that case study provided an overview of Concept of Operations development applied to ITS, explored its application to transportation problems and exposes students to the roles needed for System Engineering to proceed.
Time on Chart: 1 minute
Suggested Comments:
Interactivity:
Additional Resources:

## Slide 23: References
International Council on Systems Engineering (INCOSE) - http://www.incose.org/
Systems Engineering for Intelligent Transportation Systems Handbook - https://ops.fhwa.dot.gov/publications/seitsguide/
Systems Engineering Guidebook for Intelligent Transportation Systems (ITS) - https://www.fhwa.dot.gov/cadiv/segb/
Notes: Purpose of Slide: Provide some references for systems engineering and ITS
Key Message: For more information on systems engineering check out the International Council on Systems Engineering (INCOSE). INCOSE champions the art, science, discipline, and practice of systems engineering. References are provided for both the Systems Engineering for Intelligent Transportation Systems Handbook and the Systems Engineering Guidebook for Intelligent Transportation Systems (ITS), both endorsed by the Federal Highway Administration (FHWA).
Time on Chart: 1 minute

## Slide 24: References
United States Department of Transportation (USDOT) Intelligent Transportation Systems (ITS) Joint Program Office (JPO) - http://www.its.dot.gov/index.htm
USDOT ITS JPO Professional Capacity Building (PCB) - https://www.pcb.its.dot.gov/
  Case Studies including this one can be found under “ITS in Academics”
National Highway Institute (NHI) - https://www.nhi.fhwa.dot.gov/home.aspx
Notes: Purpose of Slide: Provide some references for systems engineering and ITS
Key Message: For more information on ITS look at the United States Department of Transportation (USDOT) Intelligent Transportation Systems (ITS) Joint Program Office (JPO) website including their Professional Capacity Building (PCB) training area. The National Highway Institute (NHI) provides training courses including ITS to transportation professionals.
Time on Chart: 1 minute